## Slide 1: Tracking surgical instruments using NCC
Shushan Toneyan, Judith Bergadà, Madleina Caduff

## Slide 2: Initial ideas
RANSAC and Harris Corner
  RANSAC: track the shaft of the tool
  Harris Corner: find the corner of the central tweezer
Notes: Which training images to use? -> tool moves and rotates -> difficult to have that many training images which cover all possible positions

## Slide 3: RANSAC and Harris corner
Notes: RANSAC and Harris Corner:
- Both worked, but not very robust. Don‘t make use of previous images.

## Slide 4: Initial ideas
RANSAC and Harris Corner
  RANSAC: track the shaft of the tool
  Harris Corner: find the corner central tweezer
Normalized Cross Correlation (NCC)
  Template matching
Notes: Which training images to use? -> tool moves and rotates -> difficult to have that many training images which cover all possible positions

## Slide 5: Algorithm: NCC with “memory”
1st image: take “small” patch around starting position  use it as template for 2nd image
for image in images:
  take “large” patch in new image centred at the position of previous match
  compute NCC between this “large” patch and the templates ( = previous 15 matches)
  select “small” patch with maximum NCC
  save centre of match
  add “small” patch to templates
Notes: Draw algorithm on the board or add little animation
Extremely smart, because it accounts for little changes in instrument orientation / illumination / reflectance etc. instead of fixed training images

## Slide 6: Challenges
Grayscale images
Slight deviations
  Instead of using just the previous image, use 15 last images for template matching
Notes: Grayscale -> less noisy

## Slide 7
Notes: Qualities: perfect for A, nearly perfect for B. Very generic, will most probably also work for other image sets. No training images required, uses the information contained in the images itself.
Limitations: First image needs to have a known starting position.

## Slide 8: Summary
Very generic method, high accuracy
Could be improved by:
  More robust: find back when loosing track (i.e. use Harris Corner and RANSAC)