## Slide 1: Tracking surgical instruments using NCC
Shushan Toneyan, Judith Bergadà, Madleina Caduff

## Slide 2: Initial ideas
RANSAC and Harris Corner
  RANSAC: track the shaft of the tool
  Harris Corner: find the corner of the central tweezer

## Slide 3: RANSAC and Harris corner
Notes: RANSAC and Harris Corner:
- Both worked, but not very robust. Don‘t make use of previous images.

## Slide 4: Initial ideas
RANSAC and Harris Corner
  RANSAC: track the shaft of the tool
  Harris Corner: find the corner central tweezer
Normalized Cross Correlation (NCC)
  Template matching
Notes: Which training images to use? -> tool moves and rotates -> difficult to have that many training images which cover all possible positions

## Slide 5: Algorithm: NCC with “memory”
1st image: take “small” patch around starting position  use it as template for 2nd image
for image in images:
  take “large” patch in new image centred at the position of previous match
  compute NCC between this “large” patch and the templates ( = previous 15 matches)
  select “small” patch with maximum NCC
  save centre of match
  add “small” patch to templates
Notes: Extremely smart (!!!), because it accounts for little changes in instrument orientation / illumination / reflectance etc. instead of fixed training images

## Slide 6
15 Templates
NCC Calculation
Notes: We start with a previously found point (red small dot that was found in step before) and 15 templates
Put a larger frame around the red dot
The red point disappears and the tool moves slightly but the green larger frame remains as it was
The green frame is cut out and flies to the templates
NCC
A smaller patch from the frame is chosen as the best and an arrow indicates that this is where the new red dot appears (no green frame needed)
The smaller template is added to the 15 templates, all move to the left and the last one is removed

## Slide 7: Challenges
Use grayscale images
Slight deviations
  Instead of using just the previous image, use 15 last images for template matching
Notes: Grayscale  less noisy

## Slide 8
Notes: Qualities:
Performs very good for both A and B
generic, will most probably also work for other image sets
No training images required, uses the information contained in the images itself
Really fast (4s per set)
Limitations:
First image needs to have a known starting position
if there is a huge change in the first few frames, it might be difficult without any training images.

## Slide 9: Summary
Very generic method, high accuracy, fast
Could be improved by:
  More robust: find back when loosing track (i.e. use Harris Corner and RANSAC)